## Slide 1: Autonomous Landing of NASA GTM Aircraft
Agah Enes SOYALP
Ebubekir DENİZHAN
Furkan ÇİFTLİKCİ
Assoc. Prof. İlker ÜSTOĞLU

## Slide 2: Table of Contents
1. Introduction
2. Modelling of GTM Aircraft
3. Trim and Linearization
4. Aircraft Modes
5. Landing Phases
6. Open-Loop Analysis
7. Flight Controller Design
8. Simulation and Results
Figure 1: Overview of an aircraft from bottom

## Slide 3: Introduction
Mathematical Modelling and Linearization
Controller Design
Simulation and Performance Analysis
Results and Evaluation
Figure 2: NASA GTM T-2 Model Aircraft
Figure 3: Accidents by phase of flight

## Slide 4: Modelling of GTM Aircraft
The most complex and expensive model!
The SIMULINK model is almost completely close to reality.
Flight Dynamics literature review!
Figure 4: All aircrafts developed for simulation
Figure 5 & 6: SIMULINK Model of GTM T-2

## Slide 5: Trim and Linearization
Definition: A trim point of an Aircraft is the state where all resultant forces and moment are equalst to zero
Trim Conditions:
Straight and Level Flight
Pull-up / Push-over Maneuvers
Figure 7: Trim & Lineerization
Steady-state Turn
Steady Heading Sideslip

## Slide 6: Aircraft Modes
Longitudinal Modes
Root Location | Natural Frequency | Damping Ratio | Period
-0.022234 0.30826i | 0.30906 | 0.07193 | 20.33
Root Location | Natural Frequency | Damping Ratio | Period
 | 0.30906 | 0.07193 | 20.33
Root Location | Natural Frequency | Damping Ratio | Period
-2 6.0102i | 6.6142 | 0.41749 | 0.94995
Root Location | Natural Frequency | Damping Ratio | Period
 | 6.6142 | 0.41749 | 0.94995
Phudoid Mode
Short-Period Mode
Figure 8: Phugoid Mode
Figure 9: Short-Period Mode

## Slide 7: Aircraft Modes
Lateral Modes
Roll Mode
Dutch-Roll Mode
Root Location | Natural Frequency | Time Constant
-5.8107 | 5.8107 | 0.1721
Root Location | Natural Frequency | Damping Ratio | Period
-0.79505 5.8963i | 5.9497 | 0.13363 | 1.0561
Root Location | Natural Frequency | Damping Ratio | Period
 | 5.9497 | 0.13363 | 1.0561
Spriral Mode
Root Location | Natural Frequency | Time Constant
-0.039425 | 0.039425 | 25.364
Figure 10: Lateral Modes

## Slide 8: Landing Phases
Figure 11: Landing Phases
Base Leg
Final Approach
Flare
Touchdown

## Slide 9: Open-Loop Analysis
Angular velocities and rates according to control surfaces doublets
Figure 12: Elevator - q - theta
Figure 13: Rudder - r - psi
Figure 14: Aileron – p - phi

## Slide 10: Open-Loop Analysis
Linear velocities and rates according to control surfaces doublets
Figure 15: Elevator – u - v - w
Figure 16: Aileron – u – v - w
Figure 17: Rudder - u – v - w

## Slide 11: Flight Controller Design
Longitudinal Controllers
    Inner Loop, Pitch Attitude Hold
    Outer Loop, Altitude Hold
    True Airspeed (TAS) Control
Lateral Controllers
    Inner Loop, Wing Leveler
    Outer Loop, Heading Angle Hold
    Sideslip Angle Control

## Slide 12: Altitude Controller
Figure 18: Longitudinal Controller

## Slide 13: TAS Controller
Figure 19: True Airspeed Control

## Slide 14: Heading Angle Controller
Figure 20: Lateral Controller

## Slide 15: Sideslip Angle Controller
Figure 21: Sideslip Control

## Slide 16: Simulation and Results
Base Leg
    Heading Angle Arrangement
    Speed Adjustment
    Flaps Extension
Glide Phase
Flare Phase
Touchdown

## Slide 17: Heading Angle Arrangement
Base Leg
Figure 22: Lateral controller graphics during roll maneuver

## Slide 18: Speed Adjustment
Base Leg
Figure 23: Velocity controller graphics during speed adjustment

## Slide 19: Flaps Extension - 15°
Base Leg
Figure 24: Velocity and longitudinal controller graphics during flaps extension

## Slide 20: Glide Phase
Figure 25: Longitudinal and velocity controller graphics

## Slide 21: Flare Phase and Touchdown
Figure 26: Longitudinal and velocity controller graphics

## Slide 22: FlightGear

## Slide 23: Thank you...
Agah Enes SOYALP
Ebubekir DENİZHAN
Furkan ÇİFTLİKCİ
Assoc. Prof. İlker ÜSTOĞLU